N9699G 1974 182P Checklists

(Develop your own. For N9699G and POH)

(Formatted for Sony e-reader)

## Before Start

Seat Belts

Fuel Select: both

Trim for takeoff

Mag, Master, Radio Master off

Circuit Breakers ok

Brakes on

## Engine Start (Carburated)

Mixture Rich

Carb Heat off

Master on

Prime if cold (2-6)

Throttle 1/8 “

Area Clear, Mag Start

Check: oil pressure

700 RPM

Align DG

Avionics master on

Lean for taxi

Cowl Flaps open

## PreTakeoff (CIGAR)

Controls fullthrow

Instruments set

(Radios, Beacon)

Gas both

Attitude: Trim set for takeoff, flaps

Cowl Flaps open

Run-up 1700 rpm

Lean if high altitude

prop (check rpm,oil,mp)

mag 125 max drop,

carb heat

oil press, vacuum, Alt chk

Alternate vacuum, static

Seat belts, Door

## PreTakeoff (Lights, camera, action)

Lights: on,

Camera: Transponder on

Action: Flaps 10-20 degrees

Lift nose 60mph

Climb at 80-90mph,

60mph until obstacle clear

## PreLanding (LCGUMPS)

Landing light on

Carb Heat, Cowl Flaps

Gas selector, gas indicator check

Undercarriage: none

Mixture: enrichen for full power for go-around

Power RPM around 1800, Prop forward, MP, flaps

Seatbelts, safety check

## After Landing

Flaps up

Transponder Standby, landing light off

Cowl Flaps open, Carb Heat off

## Shutdown (SLIM)

Switches (all electrics, but master)

Lean

Ignition off

Master off

Control Lock,Fuel Left Side on 182

## Cruise (LCGUMPS)

Landing light off

Cowl Flaps closed

Gas selector, indicator check

Undercarriage: none

Mixture: Lean appropriately

Prop, MP as desired, no flaps

Seatbelts/Safety check

# Speeds (mph) 1974 182P

Vrot		63, 20°

Vx			70  2600rpm

Vy			90,  85 at 10,000

Land		70-80

Balked		63

Short TO	60  2600rpm, 20° flaps

Short Land	70

Glide		80

# N9699G Stall Speeds w/ Stol kit

20( flaps:	55 Horn, 45 break

40( flaps:	50 Horn, 40 break

# Leaning

## EI UBG-16 Leaning Operation

Mode switch right until “Lean” indication

½ turn lean, wait 5 seconds

Repeat until “Peak”

Warning blinks

Peaked cylinder will blink

Step switch right

Mode switch left

½ turn rich, wait 5 seconds

Repeat until “Peak – 100”

Use 10 degrees C Carb temp

16”	2450	51%hp  Any ROP or LOP

18”	2450	58%hp  Any ROP or LOP

20”	2450	67%hp  100 ROP

22”	2450	72%hp  125 ROP

23”	2450	78%hp  180 ROP

19”	2300	58%hp  Any ROP or LOP

(verify RPM gauge with optical Tach, many are off)

During Climb and Touch & Goes

Full Rich or (1300EGT or lower)

Taxi:

Lean aggressively

# Red Box for Leaning

At about 65% power or so, 100ºF ROP to Peak.

At about 70%, 125ºF ROP to 25ºF LOP.

At about 75%, 180ºF ROP to 40ºF LOP.

At about 80%, 200ºF ROP to 60ºF LOP.

(On most of these engines, with a properly set mixture at full rich, at sea level, full power, the EGT ends up at about 250ºF ROP, with some as high as 300ºF ROP.)

# Autopilot

## Stec 55 Operation

HDG+NAV, HDG+APR, HDG+REV

Intercept angle different than 45

Keep Heading bug on desired intercept

Until HDG symbol goes out

ALT	One extra time to force intercept GS

After APR+ALT already active

GS symbol blinks

NAV	One extra time while in APR mode

Stops glideslope intercept.

GS symbol will flash.

ALT symbol stays on.

## Autopilot Stec 55 Vertical Preselect

MAN	disable box

ALR	altitude alert

ALT	current Altitude,

press again for preselect value

DATA, DH, rotate, DATA,

Decision height warn

DATA, BAR, rotate, DATA

New altimeter setting

DATA, ALT, rotate, DATA

New preselect

VS+ALT on main Autopilot

to activate preslect

VS on main Autopilot,  rotate on Preselect

To set vertical speed.

# Emergency

## Engine Failure (ALARMS)

Airspeed: 80mph

Location to land

Air restart

(Carburated)

Prop high

Carb Heat

Fuel select full tank or other tank

Mixture: rich

Throttle: ¼

Mag: Start if not windmilling

Try only one mag

Radio set 121.5 or local frequency, 7700 Transponder

Mayday

Secure

Mag off

Mixture cutoff

Fuel select off

Master off just before landing

Open Door

## Engine Fire in Air

Mixture: off

Fuel: off

Master: off

100Mph

Heat, Fresh Air off

Speed to put out fire

Land

## Engine Fire on Ground

Continue cranking

If start, run Engine at 1700 for a few minutes

If no start, crank for 2-3 minutes throttle open

2nd person get extinguisher

When ready,

stop starter, master, ignition, fuel selector.

Extinguish and smother flames

Inspect for damage

## Electrical Fire

Master off, vents off

Other switches off (except ignition)

Check circuit breakers

Master Switches on

Select switches on successively slowly

Open vents only after fire fully out

## Excessive Rate of Charge

Turn off both sides of Master

Turn on both sides of Master

If not ok, turn off Alternator side of master

Reduce avionics that is on

# Preflight

## Some numbers

Oil Check: 182: 9-12 qts

Tire Pressure:

Main: 42psi

Front: 49psi

Strut: 55-60psi

## N9699G Weight & Balance

1847 Empty

2950 Gross

474 Max fuel

628 Max load with full fuel

## Stec 55 Autopilot preflight

HDG+VS

CWS

VS rotate cw, yoke out

VS rotate ccw, yoke in

AP disconnect

HDG

Bug left, then right

Alt

Push yoke, watch trim

Pull yoke, watch trim

# Miscellaneous

## Flight Plan

IFR,VFR

*Aircraft ID

*Plane Type/transponder: C182/G

Airspeed: 120knots

Departure point

Departure time

Altitude

Route of flight

*Destination

Time en-route

Remarks

Fuel on Board

Alternate Airport

Pilot Name, Phone number, home base

People on Board

Color of plane

## Pirep

Nearest Airport/VOR

Time if not now

Altitude/ direction of flight

Aircraft Type

Clouds

Visibility

Temperature

Wind dir/speed

Turbulence

Icing

Wind Sheer (knots loss/gain)

Destination

## Weather

Tailwind: better weather to right

Headwind: better weather to left

Standard Lapse 2C 3.5F

High Pressure- clockwise and out in North Hemisphere

Cold or Low look out below

## VFR

Class C,D,E below 10,000:

3 Mile Vis, 1000 above, 500 below, 2000 beside

Class E above 10,000:

5 Mile Vis, 1000 above, 1000 blw, 1 mile beside

0-179 	Odd Thousands+500

180-359 Even Thousands+500

MST +7 hr, MDT +6 hr

## Light Signals

Steady G:	Takeoff	Land

Flashing G:	Taxi	Return to Land

Steady R:	Stop	Give way/circle

Flashing R:	Taxi off 	Do not land

Flashing W:	Return 	-

Altern RG:	Caution	Caution

## Intercept Procedures

| Interceptor | Meaning | You | Meaning |
| --- | --- | --- | --- |
| Rocks wings, slow turn to desired direction | Turn this direction | Rock wings | Understand |
| Abrupt climbing 90° turn away | You may proceed | Rock wings | Understand |
| Circles airport, lowers gear, overflies runway | Land at this airport | Lower gear, land | Understand |

| You | Meaning | Interceptor | Meaning |
| --- | --- | --- | --- |
| Raise gear while overflying runway 1000’ AGL, flash lights | Airport not ok | Goes to other airport | Understand |
| Flash lights regular intervals | Cannot comply | Abrupt climbing 90° turn away | Understand |
| Flash lights irregular intervals | In distress | Abrupt climbing 90° turn away | Understand |

## Altimeter/Compass Errors

ANDS- accelerate- north, decelerate- south

Heading North – Compass lags turns by latitude

Heading South – Compass leads turns by latitude

## SPOT

ON: push on button, wait 2 seconds

OFF: push on button for 3 seconds

911: push 911 button for 2 seconds

911 off: push 911 button for 3 seconds

Help: push Help button for 2 seconds

Help off: push Help button for 3 seconds

OK: press Ok button briefly

Tracking: press Ok button for 5 seconds

Tracking off: press ok for 3 seconds

Do OK once before and after Tracking

Wait for OK light to stop blinking before track

## Frequencies/Transponder

122.0	Enroute Flight Advisory: weather (xxx FlightWatch)

122.2	FSS- weather, flight plans (xxx Radio)

121.5	Emergency

122.8	Multicom for airports without Unicom/CTAF

122.1	Receive Only for FSS

122.75	Plane to plane

122.85	Plane to plane

121.7,.8,.9 Ground

122.7	BDR

122.75	FNL

122.975 LMO (AWOS 120.0)

1200 VFR

7500 Hijack

7600 Radio Failure

7700 Emergency

0000, 7777 Do not use

# Mnemonics

WRIMTIM 
weather, radio comms and navs, instruments, missed approach point, time, inbound course, minimum altitude 
UNOS 
undershoot north, overshoot south (by lattitude for standard rate turn) 
ANDS 
accelerate north, decelerate south 
ALARMS 
airspeed, landing site, air restart, radios, mayday, secure plane 
ARROW 
air worthiness, registration, radio certificate (only outside US now), owners manual, weight/balance 
TTTTT 
turn, time, twist, throttle, talk 
CRAFT 
cleared to, route, altitude, frequency, transponder 
CIGAR 
controls, instruments, gas, attitude (trim and flaps), runup 
LCGUMPS 
Landing light, carb heat/cowl flaps, gas, undercarriage, mixture, prop/power, safety 
SLIM 
switches, lean, ignition off, master off 
PARE 
power, aileron, rudder, elevator 
TOMATOFLAMES 
tach, oil press, manifold press, altimeter, temp, oil pressure, fuel guage, landing gear position, air speed, magnetic compass, elt, seat belts 
FLAPS night time equipment 
fuses, landing light (if for hire), anticollision lights, position lights, source of electricity 
GRABCARD ifr equipment 
generator, radios, attitude indicator, ball, clock, adjustable altimeter, rate of turn indicator, directional gyro 
IMSAFE 
illness, medication, stress, alcohol, fatigue, eating 
RAWFAT (preflight requirements) 
runway lengths, alternates, weather, fuel requirement, atc delays, takeoff/landing distance data 
CCCC (Missed approach start) 
cram it, clean it, cool it, call it 
AVEF (IFR route for lost comms) 
assigned, vectored, expected, filed 
MEA (IFR altitude for lost comms) 
minimum, expected, assigned